## Slide 1: A-MPDU Aggregation
Problems in the creation of the A-MPDU frames

## Slide 2: Our objective and context
To create a “fake” AP using a wireless device in monitor mode
make it able to manage the association with a normal 802.11n device
Send a number of A-MPDUs to it, and study the savings in terms of air time and efficiency
The source code is being shared here
  https://github.com/Wi5/wi5-aggregation
This is part of a Final Degree Project in Unizar.es. It is also a collaboration with Wi-5 project.

## Slide 3: Hardware
As an AP:
  TP-Link TL-WN722N with the driver ath9k_htc working in monitor mode
As the STA:
  AR9287 Wireless Network Adapter (PCI-Express) rev 01 with the driver ath9k working in managed mode

## Slide 4: Traffic Scheme (Connection & Data)
AP
STA
Beacon
Probe Request
Probe Response
ACK
Auth. Request
ACK
Auth. Response
ACK
Assoc. Request
ACK
Assoc. Response
ACK
AP
STA
ADDBA Request
ACK
ADDBA Response
ACK
A-MPDU
BA Request
BA
Our problem is in the creation of this frame (including two IP packets)

## Slide 5: Beacon Packet (Fields and values we fill)
Radiotap Header
IEEE 802.11 MAC Header
IEEE 802.11 Management - Beacon
-Version: 0
-Length: 9 (Radiotap Header + Data Rate)
-Present flags: Only a 1 in Rate
-Data Rate = 108 in decimal
-Version: 0
-Type: Management
-Subtype: Beacon
-Duration: 0x0000
-Destination Address: ff:ff:ff:ff:ff:ff
-Transmitter Address: Our MAC
-Source Address: Our MAC
-Sequence number
-Timestamp: Current Timestamp
-Interval: 102.4 ms.
-Capabilities: ESS, Immediate Block ACK & QoS
-SSID: ap0
-DataRates
-Channel: 5

## Slide 6: Probe Response (Fields and values we fill)
Radiotap Header
IEEE 802.11 MAC Header
IEEE 802.11 Probe Response
-Version: 0
-Length: 9 (Radiotap Header + Data Rate)
-Present flags: Only a 1 in Rate
-Data Rate = 108 in decimal
-Version: 0
-Type: Management
-Subtype: Probe Response
-Duration: 0x0000
-Destination Address: ff:ff:ff:ff:ff:ff
-Transmitter Address: Our MAC
-Source Address: Our MAC
-Sequence number
-Timestamp: Current Timestamp
-Interval: 102.4 ms.
-Capabilities: ESS, Immediate Block ACK & QoS
-SSID: ap0
-DataRates
-Channel: 5

## Slide 7
Auth. Response (Fields and values we fill)
Radiotap Header
IEEE 802.11 MAC Header
IEEE 802.11 Management
-Version: 0
-Length: 9 (Radiotap Header + Data Rate)
-Present flags: Only a 1 in Rate
-Data Rate = 108 in decimal
-Version: 0
-Type: Management
-Subtype: Authentication
-Duration: 0x0000
-Destination Address: STA MAC
-Transmitter Address: Our MAC
-Source Address: Our MAC
-Sequence number
-Auth. Algorithm: Open System
-Auth. SEQ: 0x0002
-Status Code: Successful

## Slide 8: Assoc. Response (Field and values we fill)
Radiotap Header
IEEE 802.11 MAC Header
IEEE 802.11 Management
-Version: 0
-Length: 9 (Radiotap Header + Data Rate)
-Present flags: Only a 1 in Rate
-Data Rate = 108 in decimal
-Version: 0
-Type: Management
-Subtype: Association Response
-Duration: 0x0000
-Destination Address: STA MAC
-Transmitter Address: Our MAC
-Source Address: Our MAC
-Sequence number
-Timestamp: Current Timestamp
-Interval: 102.4 ms.
-Capabilities: ESS, Immediate Block ACK & QoS
-Status code: Successful
-SSID: ap0
-DataRates
-Channel: 5

## Slide 9: AddBA Request (Fields and values we fill)
Radiotap Header
IEEE 802.11 MAC Header
IEEE 802.11 Management
-Version: 0
-Length: 9 (Radiotap Header + Data Rate)
-Present flags: Only a 1 in Rate
-Data Rate = 108 in decimal
-Version: 0
-Type: Management
-Subtype: Action
-Duration: 0x0000
-Destination Address: STA MAC
-Transmitter Address: Our MAC
-Source Address: Our MAC
-Sequence number
-Category Code: Block ACK
-Action Code: Add Block ACK Request
-Dialog Token: 0x01 and increases in AddBA Request package sent
-Block ACK Parameters: 0x1002 (means Inmediate Block ACK and the order of the buffer)
-Block ACK Timeout: 0x0000
-Block ACK SSC: The following number of sequence of this frame

## Slide 10: A-MPDU (I): structure with two IP packets
Radiotap Header
IEEE 802.11 QoS MAC Header
IP Header
A-MPDU Delimiter
LLC
SNAP
UDP Header
Datagram
We repeat this twice in the same frame
-Version: 0
-Length: 9 (Radiotap Header + Data Rate)
-Present flags: Only a 1 in Rate
-Data Rate = 108 in decimal
-Reserved&Lengh: 0x4004
-CRC: 0x47
-Delimiter Signature: 0x4E (‘N’)
All these values were taken from an example
-Version: 0
-Type: Data
-Subtype: QoS
-Duration: 0x0000
-Destination Address: STA MAC
-Transmitter Address: Our MAC
-Source Address: Our MAC
-Sequence number
-QoS: 0x0000

## Slide 11: A-MPDU (II): structure with two IP packets
Radiotap Header
IEEE 802.11 QoS MAC Header
IP Header
A-MPDU Delimiter
LLC
SNAP
UDP Header
Datagram
We repeat this twice in the same frame
-DSAP: 0xAA
-SSAP: 0xAA
-Control: 0x03
-OID: 0x000000
-Protocol ID: 0x0800
-Internet Header Length (IHL): 5
-Version:4
-ToS:0x00
-Total Length: IP Header Length + UDP
Header Length + Data Length
-ID
-Frag_off: 0
-TTL: 255
-Protocol: UDP
-Source Address: Our IP Address
-Destination Address: The STA IP Address
-Checksum

## Slide 12: A-MPDU (III): structure with two IP packets
Radiotap Header
IEEE 802.11 QoS MAC Header
IP Header
A-MPDU Delimiter
LLC
SNAP
UDP Header
Datagram
We repeat this twice in the same frame
-Source Port: 6666
-Destination Port: 8622
-Length: UDP Header Length + Data Length
-Checksum
In this example 8 zeros due to the fact of using the example A-MPDU delimiter values

## Slide 13: A-MPDU (IV): Questions
This frame is giving us the problems, it could be happening because we didn’t notice that some flag of this frame or the previous ones must be enabled, we tried to enable in this frame the “A-MPDU status” that belongs to the radiotap header but we couldn't.
Other thing that could be wrong are the values of the A-MPDU delimiter but we try to use the values used in the following program as we said previously:
  https://github.com/rpp0/aggr-inject
But even using those values, Wireshark thinks that the A-MPDU delimiter is the Frame Control Field, as you can see in the attached capture. Wireshark thinks there were Fragmented IEEE802.11 frames

## Slide 14: BA Request
Radiotap Header
IEEE 802.11 MAC Header
IEEE 802.11 BAR Frame
-Version: 0
-Length: 9 (Radiotap Header + Data Rate)
-Present flags: Only a 1 in Rate
-Data Rate = 108 in decimal
-Version: 0
-Type: CTL
-Subtype: BAR
-Duration: 0x0000
-Destination Address: STA MAC
-Transmitter Address: Our MAC
-Source Address: Our MAC
-Sequence number
-BAR Control: 0x0001 (means Immediate Block ACK)
-Block ACK SSC: First MPDU sequence number

## Slide 15: THANKS FOR YOUR HELP